## Slide 1: Real-Time Video Quality of Experience Monitoring for HTTPS and QUIC
M. Hammad Mazhar
The University of Iowa
Zubair Shafiq
@HmdMazhar
@zubair_shafiq
Notes: Good afternoon everyone,
I will be presenting our work on ‘Real Time Video Quality of Experience Monitoring for HTTPS and QUIC’ today. In this work, we tackle the problem of real-time video QoE metric prediction for encrypted video streaming using machine learning. Our approach leverages features based on the network and transport layer and can accurately predict QoE metrics upto 90% of the time

## Slide 2: Overview – Video Streaming
72% of all consumer Internet traffic was video in 2016
Forecasted to grow up to 81% by 2021.
Today’s Internet is a ‘video’ Internet
Notes: Over recent years, we have seen a phenomenal rise in video traffic in today’s Internet.
In 2016, 72% of all consumer Internet traffic was video
Over the next few years, video traffic is forecasted to grow up to 81% by 2021.
This growth is driven by major video streaming services and content providers, such as Netflix, YouTube, and Twitch.
In short, today’s Internet is a ‘video’ Internet

## Slide 3: Overview - Ecosystem
Users
Internet Service Provider Networks
Content Providers
Notes: In the current Internet video streaming ecosystem, we have 3 major stakeholders
Content Providers, who host and serve video content.
Users, which access this video content through devices like PCs and smartphones.
Internet Service Provider Networks, through which video traffic flows from the providers to the users

## Slide 4: Overview – Adaptive Video Streaming
1080p
720p
480p
Manifest
1
2
3
…
…
…
…
Video X
Time
Time
GET Manifest
Manifest
GET 1, 1080p
GET 2, 1080p
GET 3, 720p
…
Video Buffer
Notes: The dominant framework for today’s video streaming services is adaptive video streaming.
In this framework, video content providers host video content as chunks (of equal duration), encoded at various resolutions.
Details of these video chunks and quality levels is stored in manifest files.
A client requesting video content first receives the manifest for that content.
Based on the information in the manifest, it then requests successive chunks of video.
To determine the quality of requested video chunks, the client uses some adaptive bitrate logic, or ABR logic.
This logic takes factors into account such as observed chunk throughput and current video buffer state
In this example, we see that the client reduced the quality of video from 1080p to 720p from the 3rd chunk onwards.
This could be likely due to lower throughput experienced in downloading the second chunk.

## Slide 5: Overview – Quality of Experience Metrics
Used to objectively measure user experience.
Startup Delay
Average Quality
Rebuffering
QoE metrics
=1080p
=900p
Notes: A key driver in the popularity of a streaming service is its quality of user experience.
While user experience is a highly subjective measure, it can be captured in some form using objective metrics.
In current literature, some of these metrics are:
Startup delay, which is the time it takes for video playback to start from the time the user clicks the play button.
Average Quality, which measures the resolution of the video stream on average in a fixed time window. In this example, if our time window is equal to two chunks of video, then over the first two chunks, the average quality is 1080p. When we shift the window over the second and third chunk of video, the average quality of this window is now 900p.
Rebuffering events ,when the video buffer runs out of data to continue playback, and must wait to be replenished to continue.
Collectively, these metrics (startup delay, average quality and rebuffering) are part of what are known as Quality of Experience metrics

## Slide 6: Overview - Network Management
QoE metrics
Application
Transport
Network
Link
Physical
Application
Transport
Network
Link
Physical
Application
Transport
Network
Link
Physical
User
ISP
Content Provider
DPI
HTTPS
QUIC
QoE metrics
QoE metrics
LTE Networks
Notes: Coming back to the ecosystem, we now look at the network stack at each stakeholder.
Users and content providers have explicit knowledge of QoE metrics, at the application layer, and use these metrics to improve the experience through client side and server side strategies, but the network in between the two would like to get such metrics to improve its own performance.
Traditionally, network operators infer QoE metrics through the use of deep packet inspection boxes, which can process information from the application and transport layer to infer these metrics.
Based on these QoE metrics, the network can then optimize or shape the network to achieve certain objectives such as stability and performance in the network and for the user.
This is common for LTE networks, where network operators use DPI boxes to allocate resources across users on the limited radio spectrum
However, with the rise of awareness of privacy concerns amongst users, there has been an increase in use of end to end encryption.
At the application layer, this is implemented through HTTPS. Which then reduces application layer visibility for the network.
End to end encryption has also extended to the transport layer, with protocols such as QUIC.
Under such protocols, the ISP no longer has visibility at the application and transport layer, which makes DPI useless.
This loss in visibility leaves the ISP incapable to optimizing its network to improve user experience.

## Slide 7: Challenge - Encryption on the rise
HTTPS page loads increased from 45% (2016) to 69% (2018).
YouTube is increasingly using QUIC for mobile video delivery.
End-to-end encryption eliminates QoE monitoring.
Notes: At the same time, there is evidence that end-to-end encryption will become more prevalent over time.
Already, global page loads utilizing HTTPS have increased from 45% to 69% from 2016 to 2018, as per Firefox Telemetry.
Furthermore, video content providers themselves are using end-to-end encryption, as reported by Vasona Networks, who note that Youtube video traffic on mobile networks is increasingly using the QUIC protocol.
Under these circumstances, network and network operators must devise new methods to monitor QoE metrics under end-to-end encryption protocols.

## Slide 8: Problem Statement
Predict QoE metrics in real-time for encrypted video traffic.
Assumptions:
Video stream detection on encrypted traffic (machine learning, traffic analysis, etc)
Network/Transport layer info. collection
Notes: This leads us to our problem statement.
Network operators must predict objective QoE metrics (startup delay, average quality and rebuffering). It is important to predict these metrics in real time or near real time for faster network management.
To tackle this problem, we define some assumptions regarding the capabilities of the network operator:
Network operators can determine if traffic streams belong to video content providers. This can be done through approaches based on machine learning,, traffic analysis etc.
For such traffic streams, network operators can collect network/transport-layer information, but cannot access packet payloads due to encryption. In the case of QUIC, only network-layer information can be collected.

## Slide 9: Our Contributions
Machine learning for QoE metric prediction
Prediction at 10 second time scales
Network/transport layer features.
Notes: With the problem and our assumptions regarding the problem defined, I present our contributions towards solving this problem.
We utilize machine learning techniques for building models to predict QoE metrics for encrypted video streaming.
We specifically focus on predictng QoE metrics at near real-time (10 second) time scales.
We utilize features based on network and transport layer information for video stream traffic.

## Slide 10: Proposed Approach
Training Phase
Training Videos
Packet Traces
Transport and network header information
Feature Extraction
Model Training
1 Model per metric
Identified
Video
Packet Traces
Transport and network header information
Feature Extraction
Deployment Phase
QoE Prediction
Startup delay
Average quality
Rebuffering
Network Management
Notes: With our contributions outlined, I present the details of our approach.
The structure of our proposed approach is as follows:
Our approach can be divided into two phases, a training phase and a deployment phase.
In the training phase, the network operator streams videos from a video content provider, collecting ground truth QoE metrics and packet traces, under diverse network conditions.
The network operator then extracts a comprehensive set of features based on transport and network layer information in 10 second windows. These features are then labelled with the ground truth QoE metrics collected earlier.
Based on these features and ground truth QoE metrics, the operator trains supervised machine learning models for predicting QoE metrics, with a unique model per metric.
In the deployment phase, the network operator identifies video streams, and collects network and/or transport information for these streams. Then after extracting features in the same manner as in the training phase, the operator uses the previously trained models and the extracted features to predict QoE metrics for the identified video streams..
The network operator can then use these predicted QoE metrics to detect and mitigate QoE impairments using network management strategies.

## Slide 11: Features
Window
Packet
Network
Layer
Byte Counts
Packet Counts
Throughput
Idle Time
Packet Inter
-
arrival times
Bytes per packet
Transport
Layer
TCP Flag Counts
Out
-
of
-
order bytes/packets
TCP Goodput
Retransmission ratio
Starting/Ending bytes
-
in
-
flight
Retransmissions per packet
Receive Window
RTT
Bytes
-
in
-
Flight
HTTPS
QUIC
Notes: Now we look at the features we developed for our approach
.
We can first divide the features we use into two broad categories based on the layer they are extracted from:
Network layer features, which are extracted from the network layer
Transport layer features, which are extracted from the transport layer
These categories are further divided into:
Window features, which are aggregated over the whole 10 second time window
Packet features, which are calculated using individual packet data.
The set of features we consider is shown.
Note that the layers encrypted in a protocol will affect which features we can use for that protocol. Hence, models trained for HTTPS can utilize all features, while models for QUIC can only use network-layer features.
For further details on how we utilize these features, you can look in the paper.

## Slide 12: QoE Metric Prediction
We view it as a binary classification problem
Startup delay: is it below k seconds?
Average Quality: is it above a set resolution?
Rebuffering: has rebuffering occurred?
Notes: The basic problem that we are attempting to solve is of QoE metric prediction.
In our approach, we view this problem as a binary classification problem.
For Startup delay, we can view the problem as predicting whether Startup delay is below k seconds, where k can be changed based on requirements.
For average quality, we can view the problem as predicting whether the average quality is above or below a certain resolution in the time window.
Finally, prediction rebuffering is simply predicting whether rebuffering has occurred in the time window.
For exact details on the value of k and the resolution that we consider, I invite you to go through our work.

## Slide 13: Evaluation – Data Collection
Selenium with Google Chrome for YouTube video streaming.
Packet capture with tcpdump
Network shaping with tc and netem
Ground truth QoE metrics with YouTube IFrame API
Notes: For evaluating our approach, we collected data for video streams under different network conditions.
We streamed YouTube video over HTTPS and QUIC using the Google Chrome browser in an automated fashion using Selenium.
To capture packet traces for these video streams, we used tcpdump.
In order to stream video under different network conditions, we shaped the network traffic using the tc and netem tools.
Finally, we extract ground truth video QoE metrics using Youtube’s iFrame API.

## Slide 14: Evaluation - Machine Learning
Supervised machine learning using decision trees.
Avoid overfitting with AdaBoost ensemble meta-classification.
Evaluated under 10-fold cross validation.
Notes: Our supervised machine learning approach builds QoE prediction models as decision trees, which have shown good performance on similar problems and also have the added benefit of being human interpretable.
To develop models that do not overfit on training data, we use AdaBoost ensemble learning as a meta classifier.
Finally, to evaluate the performance of our models, we train and test these models under 10-fold cross validation.

## Slide 15: Results
Precision
Recall
QoE
Metric
HTTPS
QUIC
Precision
Recall
Precision
Recall
Startup Delay
82%
82%
85%
85%
Average Quality
85%
86%
72%
72%
Rebuffering
90%
90%
80%
80%
More results and insights in paper
Notes: Our performance metrics of choice are precision and recall, where precision, which is the ratio of true positives over true positives plus false positives, measures the ability of the model to predict correctly, and recall, which is the ratio of true positives over true positives plus false negatives, measures the ability of the model to predict for all possible cases.
We present our best results for each QoE metric, under both encryption at the application layer as in HTTPS, and encryption at the application and transport layer as in QUIC.
For Startup delay, models trained with our approach performed with ~81% precision and recall for HTTPS, and ~85% precision and recall for QUIC.
Note that performance is higher by 3% for QUIC.
(Why? Due to distribution in dataset. QUIC had a smaller class imbalance than HTTPS.)
For average quality, we see 85% precision/recall for HTTPS, and 72% precision/recall for QUIC
.
(The difference in performance here is likely due to the use of transport layer features.)
And finally when predicting rebuffering, our trained models performed with ~90% precision/recall for HTTPS, and ~80% for QUIC.
(Again, the difference in performance is likely due to the use of transport layer features.)

## Slide 16: Limitations
Differences across video providers
  Solution: Unique models per provider
Sensitive to changes in video delivery for same provider
  Solution: Online Learning
Models provide actionable insights, but not root causes
Notes: While our approach performed really well at QoE metric prediction, there are some limitations in our approach.
Video content providers differ in their video delivery mechanisms and encoding standards. To account for these differences, we can train models unique to each provider(, so we would different models for Youtube and different models for Netflix).
Following from the previous point, a video content provider can change how they deliver video over time. To account for this, models can be trained in an online fashion (or retrain models over time with newer data).
Decision tree models are human interpretable, and provide valuable, actionable insights for network providers to improve their networks to prevent QoE impairments. They cannot however show the root causes of these impairments. This limitation is a subject for future work in the area.

## Slide 17: Conclusion
Machine learning based QoE prediction for encrypted video streams
Features based on the transport/network layer
Achieve 90% accuracy for HTTPS, 85% for QUIC

## Slide 18: Questions?
Find me on Twitter: @HmdMazhar
Email: muhammadhammad-mazhar@uiowa.edu
Site: cs.uiowa.edu/~mmazhar